Test Plan Overview

Hardware:
Main Board:
-Visually inspect board for issues or inconsistencies with layout
-Verify connections, (continuity)
-Populate board
-Verify Solder connections
-Verify power levels
-Verify clock signal presence
-Verify clock signal frequencies
-Attempt to upload test binary
  -If upload successful run “Hello world”/blink program
  -Upload real firmware

Daughter Boards:
-Visually inspect board for issues or inconsistencies with layout
-Verify connections, (continuity)
-Populate board
-Verify Solder connections
-Verify power levels
-Verify clock signal presence
-Verify clock signal frequencies
-Connect daugter board to “known good” device such as Arduino, verify readings, etc.

Main board and ADC sensor:
-Sample ADC sensor, verify against “known good” values

Main board and I2C sensor:
-Sample I2C sensor, verify against “known good” values

Full Assembly, (Hard Faults)
-Remove Power
-Remove ADC sensor while running
-Remove ADC sensor during sampling
-Remove I2C sensor while running
-Remove I2C sensor during sampling
-Remove SD Card while running
-Remove SD Card while sampling
-Observe behavior near brown-out power levels
- Attempt to sample nonexistent sensors
-Attempt to read from bad I2C addresses

Software (Full assembly):
-Sample ADC sensor, verify against “known good” values
-Sample I2C sensor, verify against “known good” values
-Verify SD card data present/consistent
-Verify accuracy of timestamps
-Verify naming of data on card
-Eavesdrop serial communication from “known good” platform
-Attempt to inject intentional error conditions, bad chars, memory locations, etc.